## Slide 1: 5G-MOBIX GR-TR CBC Webinar
OBU/RSU development and
Assisted Border crossing UC
Kostas Trichias (Technical Coordinator – WINGS ICT Solutions) GR-TR Webinar, June 29th, 2020

## Slide 2: Layout
Overview information
OBU / RSU Development
  IMEC OBU (Platooning UC)
  WINGS OBU (Assisted Border Crossing UC)
  IMEC RSU (Platooning UC)
Assisted “zero touch” truck border crossing UC
  UC Overview, Diagram and info flow
  Platform development & functionality
  Early implementation video
GR-TR Webinar – June 29th 2020 – slide 2

## Slide 3: OBU/RSU/APP overview information
HW & SW developed for the GR-TR CBC
  2 OBUs (IMEC + WINGS)
  3 RSUs (IMEC)
  3 Applications (WINGS, ICCS, Tubitak)
IMEC developed OBU and RSUs will focus on the provisioning of the “Platooning with See-what-I-See” & “Autonomous truck routing in customs” Use cases
WINGS developed OBU will focus on the provisioning of the “Assisted – zero touch- truck border crossing” use cases
Application development
  Platooning (FORD) + See-what-I-See (ICCS)  already presented
  Truck routing in customs site (TUBITAK)  already presented
  Assisted – zero touch- truck border crossing (WINGS)
GR-TR Webinar – June 29th 2020 – slide 3

## Slide 4: OBU / RSU Development

## Slide 5: IMEC OBU Architecture
IMEC OBU
  offers V2X wireless communications capabilities (5G Uu and C-V2X PC5)
  has communication processing unit and can provide logging
  4G is used for remote recovery
  its switch can be connected to an external sensor/camera for streaming application
Ford’s vehicle infrastructure
  MicroAutoBox acts as an ECU (connected to truck’s CAN) that will process sensor information
IMEC’s OBU is connected to Ford’s ECU (MicroAutoBox), acting as a gateway to forward information from and to the truck
GR-TR Webinar – June 29th 2020 – slide 5

## Slide 6: IMEC OBU Specifications
Hardware:
  V2X processing unit: NUC7iDNKE
  Ethernet Switch: Phoenix gigabit switch
  C-V2X: Cohda MK6C
  4G module: Mikrotik wAP LTE kit
  Positioning System: Navilock NL-8012U GPS
  5G Modem: Quectel RM500Q.
OBU will be put inside Ford’s trucks
Antennas will be on top of the truck
GR-TR Webinar – June 29th 2020 – slide 6

## Slide 7: WINGS OBU development
WINGS developing OBU for the Assisted border crossing use case including the multitude of sensors (GPS, CO2, Proximity, NFC)
To be integrated with the FORD truck and IMEC OBU
Main functions
  Send driving instructions to FORD truck ECU
  Assess “Risk level” of each incoming truck based on collected information. Indicate proper inspection level based on outcome
  Protect customs agents based on Proximity and GPS readings
Status
  Functionality ready
  Upgrade with 5G chipsets ongoing (Quectel RM500Q)
OBU
CO2 Sensor
Proximity Sensor
GPS
ECU connector
NFC reader
GR-TR Webinar – June 29th 2020 – slide 7

## Slide 8: RSU Architecture
3 RSUs to be deployed at the Turkish border customs site
RSUs will be installed at the side of the road and will be able to provide a network uplink for the LIDAR
equipped with communications modules, including the 5G modem, and the C-V2X PC5 unit
GR-TR Webinar – June 29th 2020 – slide 8

## Slide 9: RSU Specifications
Hardware:
  Embedded PC
  5G Modem: Quectel RM500Q
  C-V2X: Cohda MK6c
  VLP-16 Lidar
  Managed Switch
  Managed PDU
  PC Engines APU2 (Recovery System)
The C-V2X module and 5G-modem will be connected to external antennas using coax cable. This is done to optimise the coverage of these modules
LIDAR will be mounted to the mounting pole using a specialised mounting bracket
GR-TR Webinar – June 29th 2020 – slide 9

## Slide 10: Assisted – zero touch- truck border crossing UC UC Overview & Scenarios

## Slide 11: Assisted “zero-touch” Border Crossing
Utilize AI & predictive analytics techniques to perform threat classification of incoming vehicles at the customs sites
Ingest heterogeneous information from:
  Vehicle On-Board Unit (OBU) and connected sensors
  Road-Side Infrastructure (RSI) and connected sensors
  Neighbouring authorities
Enable state-of-the-art services such as:
  Detection of human or livestock smuggling attempts
  Detection of cargo smuggling attempts (contraband)
  Customs agents protection from (autonomous) vehicles
Provide seamless “zero-touch” access (no inspection) through the borders to legitimate vehicles
GR-TR Webinar – June 29th 2020 – slide 11

## Slide 12: Scenario 1: Human/livestock smuggling detection
In case human / livestock presence is detected (in vehicle or cargo haul) issue a “High Risk” alert and instruct further inspection (resulting in autonomous driving instructions)
In case NO human / livestock presence is detected , issue a “Low Risk” notification and instruct a –zero touch- border crossing (resulting in autonomous driving instructions)
Perform Risk / Threat assessment based on input from CO2 sensor and truck manifest
GR-TR Webinar – June 29th 2020 – slide 12

## Slide 13: Scenario 2: Cargo smuggling detection
In case unauthorized cargo is detected issue a “High Risk” alert and instruct further inspection (resulting in autonomous driving instructions)
In case NO unauthorized cargo is detected , issue a “Low Risk” notification and instruct a –zero touch- border crossing (resulting in autonomous driving instructions)
All cargo in a vehicle (or cargo haul) is identified based on a wireless technology (e.g. NFC)
Identified cargo inventory cross-checked with the vehicle’s documentation / manifest (potentially received from neighboring country)
GR-TR Webinar – June 29th 2020 – slide 13

## Slide 14: Scenario 3: Customs agents protection
Customs agents location monitored via Proximity & GPS readings
Once the vehicle’s trajectory is determined to potentially lead to a collision or an accident with customs agents an alert is issued.
Autonomous vehicles are instructed to stop or change course
GR-TR Webinar – June 29th 2020 – slide 14

## Slide 15: UC Flow Diagram

## Slide 16: Assisted – zero touch- truck border crossing UC UC Architecture & Information flow

## Slide 17
Direct Interconnection
GR side - Cosmote
TR side - Turkcell
Customs site – Road side infra
Proximity
WINGS Cloud Platform (STARLIT) WINGS facilities in Athens
License plate recognition
gNB
MEC
Core functions (SGW / PGW)
Core functions (SGW / PGW)
gNB
Overall Architecture including ALL components
On-Board Sensors (OBU)
GR-TR Webinar – June 29th 2020 – slide 17

## Slide 18
Direct Interconnection
GR side - Cosmote
TR side - Turkcell
Customs site – Road side infra
Proximity
On-Board Sensors (OBU)
WINGS Cloud Platform (STARLIT) WINGS facilities in Athens
License plate recognition
gNB
MEC
Core functions (SGW / PGW)
Core functions (SGW / PGW)
gNB
Tx Info: CO2, NFC, Lidar distance, GPS coord., ECU info
Rx Info: Instruction messages, GUI info.
Tx Info: Camera picture, light status, GPS coord
Rx Info: Instruction messages for border bar and traffic light, GUI info.
Tx Info: Truck manifest (doc)
Rx Info: GUI info (incl. figs)
GR-TR Webinar – June 29th 2020 – slide 18

## Slide 19
Direct Interconnection
GR side - Cosmote
TR side - Turkcell
Customs site – Road side infra
WINGS Cloud Platform (STARLIT) WINGS facilities in Athens
Proximity
On-Board Sensors (OBU)
License plate recognition
gNB
Core functions (SGW / PGW)
Core functions (SGW / PGW)
gNB
Scenario A – Public IP
TX#1
TX#2
TX#3
RX#1
RX#2
RX#3
TX#4
TX#5
RX#4
RX#5
RX#6
GR-TR Webinar – June 29th 2020 – slide 19

## Slide 20: Assisted – zero touch- truck border crossing UC Cloud/Edge Platform & GUI

## Slide 21: WINGS Cloud/Edge platform & GUIs
Cloud Intelligence: Data ingestion and analytics SW provided by WINGS (based on STARLIT platform) resides both in a centralized cloud as well as at the edge nodes to facilitate low-latency communication. Two GUIs are provided with live feed from the Cloud platform with relevant information and sensor readings i) for the customs agents and ii) for the truck driver
  Algorithm input: GPS coordinates, CO2 readings, license plate recognized, thermal reading of the truck, NFC cargo ID, proximity to obstacle / human, truck cargo manifest
  Algorithm output: Truck threat assessment and classification. Utilized to make a decision to allow the border crossing or not (traffic light and security bar actuated) + Autonomous driving instructions
The two GUIs are depicted in detail in the video that follows
GR-TR Webinar – June 29th 2020 – slide 21

## Slide 22: Assisted – zero touch- truck border crossing UC Early implementation & testing

## Slide 23: Assisted “zero-touch” border crossing for CCAM – Large scale demo
Video URL: https://youtu.be/fRnY_jG3P0Y
GR-TR Webinar – June 29th 2020 – slide 23

## Slide 24
Thank you
Questions?