## Slide 1: 5G-MOBIX 2nd Webinar: Presentation of the ES – PT Cross Border Corridor and preliminary findings
5G-infrastructure
Juan Francisco Esteban (Telefonica) 20 May 2020

## Slide 2: Index
Network overview
MNOs interconnection
RAN deployment

## Slide 3: Network overview

## Slide 4: 5G infrastructure ES-PT CBC 5G Deployment
3GPP Deployment Option | Number of gNBs | Experimentation Frequency | MEC | Roaming
1st Phase - NSA Option 3x 2nd Phase - SA Option 2 (to be confirmed) | 8 | 4G - 1800 MHz (B3) 5G - 3.5 GHz (n78) | Distributed (Far edge & central) | HR/LBO
MEC deployment in order to accomplish with latency requirements, working as a Local Breakout of the traffic.
Multi-PLMN solution will be used in order to separate commercial traffic from trial traffic.
Roaming will be tested with Home Routing and Local Breakout procedures.
In total 8 gNB sites will be installed to cover the trial areas.

## Slide 5: 5G infrastructure ES-PT CBC E2E Architecture
5G NSA Option 3x
ETSI MEC deployed with distributed SGW with Local Breakout (SGW-LBO)
Internet
vMEC
Braga MEC
vMEC
Vigo MEC
S1-C
SGi
SGi
5G gNB
4G eNB
S1-U
P-GW
HSS
S5
S6a
S11
Madrid Lab Core
S-GW
MME
P-GW
HSS
S5
S6a
S11
Braga Lab Core
S-GW
MME
S1-U
S1-C
S1-C
5G gNB
4G eNB
S1-U
S1-U
S1-C
ITS Platform
PORTUGAL
SPAIN
SPGW
SGi(LBO)
SGi(LBO)
IP/MPLS direct interconnection
S8
S10
S6a
S6a
S10
S8

## Slide 6: MNOs interconnection

## Slide 7
GRX Provider
Centre Interconnection
Edge Interconnection
To meet CCAM requirements MNOs must direct interconnect the edge nodes across the border
Scalable but high Latency
Not so scalable but better Latency
Not scalable the best Latency
5G infrastructure MNOs Interconnection options

## Slide 8: 5G infrastructure 5G roaming scenarios
The two possibilities of roaming scenarios are going to be tested in order to clarify the best option for V2X services:
Each option has its own advantages and drawbacks:
It is foresee that Home Routing is the best solution for V2X services because the higher impact on the continuity is more critical than the lower impact on the latency.
Roaming option | Advantages | Drawbacks
Local Breakout | Is the optimum solution for latency reduction when an user is on the visited network Scalability | Service interruption during the transition (seconds)
Home routing | Continuity of the service is improved | Latency is increased proportionally to the distance towards the local network (~1ms/100km) Scalability

## Slide 9: RAN deployment

## Slide 10
5G infrastructure 5G Radio Access Network
Two 5G nodes are going to be deployed in cross-border corridors.
  One of the will cover the A3 motorway over the new bridge (UC1, UC2 )
  The other one will cover the old train bridge (UC3)
The sites are going to be the actual 4G locations.
Macro Cells.
Spectrum – 5G NR on band n78 (3600 – 3800 MHz)

## Slide 11
Two new sites are going to be deployed in cross-border corridors
  An axial site that will cover the A3 motorway over the new bridge (UC1, UC2).
  Two small cells that will provide dedicated coverage on the old train bridge (UC3)
Spectrum – 5G NR on 3.7 GHz and 4G anchor on 1800 MHz
Backhaul – 10 Gbps P2P Fiber to IP WAN/MPLS
Sync – GNSS and PTP T-GM G.8275.1
SITE_NAME | SECTOR | TYPE | LATITUDE | LONGITUDE | AZIMUTH
VALENCA_NEW_BRIDGE | 1 | MACRO | 42.02939 | -8.65064 | 175
VALENCA_NEW_BRIDGE | 2 | MACRO | 42.02939 | -8.65064 | 330
VALENCA_OLD_BRIDGE_A | 1 | SMALL CELL | 42.03507 | -8.64525 | 80
VALENCA_OLD_BRIDGE_B | 1 | SMALL CELL | 42.03507 | -8.64525 | 260
5G infrastructure 5G Radio Access Network.

## Slide 12
5G infrastructure Handover Area Adjustment
HO Area
RSRP PT [dBm]
RSRP SP [dBm]
a3OffsetRsrpInterFreq
a3TimeToTriggerRsrpInterFreq
The HO area will be initial adjusted by changing cell power and antenna electrical tilts.
Fine tuning of HO area through adjustment of A3 event offset and time to trigger.

## Slide 13
Thank you